## Slide 1
1
Ghost Vehicle in Fog Detector Using Pressure Wave Sensing Before Headlights Appear
Mentor :
Dr. C. Ganesh Kumar
Chairperson, Department of Electronics and Communication Engineering, School of Computing, Chennai
Presented by :
Akshaya M V - CH.EN.U4CCE24003
Devadharshini P - CH.EN.U4CCE24004
M Mukesh - CH.EN.U4CCE24015
Embedded Systems Project

## Slide 2
A New Paradigm
The Technology Stack
Zero-Latency Intelligence
The Edge-AI Solution
Ghost Sense Initiative
The Invisible Threat
Dense fog critically reduces visual range on highways and rural roads, rendering standard headlights ineffective.
Drivers face severely delayed detection of approaching vehicles, drastically increasing the likelihood of high-speed, catastrophic collisions.
SENSE
PROCESS
WARN

## Slide 3
SENSE
Capture invisible pressure disturbances generated by moving vehicles.
PROCESS
Execute real-time signal analysis natively on a Cortex-M core.
Utilizes highly sensitive MEMS acoustic sensors. Processes physical data locally on a Cortex-M microcontroller.
WARN
Deploys TinyML and Edge-AI directly on the chip. Triggers life-saving early warnings without relying on:
Detecting approaching vehicles before they become visible by capturing the low-frequency pressure waves they push ahead of them.
Trigger immediate driver alerts through:
Visual indicators (LEDs/Display) Audible alarms (Buzzer)

## Slide 4
Architecture & Data Pipeline
Fromphysicalpressurewavestoreal-timeEdge-AI alerts.
Zone 1
Physical Sensing
Zone 2
Edge-AI Processing
Zone 3
Alert Execution
6. Algorithmic Analysis
5. Digital Filtering
10. Result
8. Confirmation
Vehicle Approaches
Acoustic Detection
4. Data Acquisition
7. Threshold Decision
9. Early Warning
Signal Conditioning
Pressure Waves > MEMS Sensor > Signal Conditioning > Cortex-M ADC > Digital Filtering > TinyML Analysis > Vehicle Detection > LED/LCD/Buzzer Alert > Driver Safety

## Slide 5
Phase & Focus
Week
Core Activity
Literature Survey, Problem Analysis & Component Procurement.STM32/Cortex-M setup and architecture learning.
Key Milestone
Phase 3: Edge-AI(Algorithm & Alert)
Phase 1: Foundation(Research & Hardware)
Week 1-3
Week 7 - 9
Phase 2: Integration(Interfacing & Data)
Week 4 - 6
Phase 4: Finalisation(Prototype & Delivery)
Week 10 - 12
Sensor Interfacing & ADC Testing.Data Collection from live moving vehicles.Initial Signal Processing Implementation.
Vehicle Detection Algorithm (TinyML) Development.LED, Buzzer, and Display Integration.System Testing, Calibration, and Optimisation.
Complete Prototype Assembly.Result Analysis and Performance Evaluation.Report Writing and PPT Preparation.
Hardware Procured & Environment Setup
Successful Sensor Data Acquisition
Functional Detection Algorithm
Final Demonstration (Sept 20)

## Slide 6
Hardware Ecosystem
Expected Output
Early Detection : Reliable identification of approaching vehicles completely obscured by dense fog.
Immediate Alert : Distinct visual and audible warnings delivered to the driver via the edge device with zero latency.
Ultimate Impact : Significantly improved road safety and a drastic reduction in collisions under critical low-visibility conditions.
Software Ecosystem
Compute
Output UI
STM32F401 / STM32F103 Cortex-M Microcontroller
OLED Display / LCD (16×2)
Warning LEDs
Buzzer
Sensing
MEMS Microphone Sensor
MAX9814 / MAX4466
Ancillary Components
USB Programmer / ST-Link
Breadboard
Power Supply
Conditioning
LM358 Operational Amplifier Used for signal amplification
Environment
STM32CubeIDE STM32CubeMX
Programming Language
Embedded C Programming Optimized for TinyML constraints
Analysis Tools
MATLAB
Python
Used for initial signal analysis and algorithm modeling
Simulation & Debugging
Serial Terminal
PuTTY Tera Term
Proteus (optional for simulation)

## Slide 7
Thank You !