## Slide 1
1
Ghost Vehicle in Fog Detector Using Pressure Wave Sensing Before Headlights Appear
Mentor :
Dr. C. Ganesh Kumar
Chairperson, Department of Electronics and Communication Engineering, School of Computing, Chennai
Presented by :
Akshaya M V - CH.EN.U4CCE24003
Devadharshini P - CH.EN.U4CCE24004
M Mukesh - CH.EN.U4CCE24015
Embedded Systems Project

## Slide 2
The Edge-Al Solution
A New Paradigm: Detecting approaching
vehicles before they become visible by
capturing the low-frequency pressure
waves they push ahead of them.
The Invisible Threat
Dense fog critically reduces visual range
on highways and rural roads, rendering
standard headlights ineffective.
Drivers face severely delayed detection of
approaching vehicles, drastically increasing
the likelihood of high-speed, catastrophic
collisions.
SENSE: Capture invisible
pressure disturbances generated
by moving vehicles.
The Technology Stack: Utilising highly
sensitive MEMS acoustic sensors, the
system processes physical data locally
on a Cortex-M microcontroller.
Zero-Latency Intelligence: By deploying
TinyML and Edge-Al methodologies
directly on the chip, we trigger life-saving
early warnings without relying on cloud
processing or visual line-of-sight.
PROCESS: Execute real-time
signal analysis natively on a
Cortex-M core.
WARN: Trigger immediate visual
(LEDS/Display) and audible
(Buzzer) driver alerts.
INTRODUCTION
Seeing the unseen: Predicting oncoming traffic before the headlights cut the fog

## Slide 3
S.NO
Title of the Paper
Hardware
/Software
Year
Inference
1.
2.
3.
4.
5.
Objective
Ensemble Artificial Intelligence Framework for Real-Time Automatic Vehicle Detection and Classifications
https://ieeexplore.ieee.org/abstract/document/11363414
May
2026
Improve 3D object detection in fog using enhanced camera-LiDAR fusion.
Enhanced 3D perception, Virtual point clouds, Costly sensor fusion
FogFusion: Robust 3D object detection based on camera-LiDAR fusion for autonomous driving in foggy weather conditions
https://journals.sagepub.com/doi/abs/10.1177/09544070251327229
MAR
2026
Estimate road visibility and driving risk under rain-fog conditions using roadside surveillance images.
Visibility estimation, Risk assessment, Infrastructure-based monitoring
Fog-aware feature enhancement, Real-time detection, Camera limitations
Dynamic Visibility Recognition and Driving Risk Assessment Under Rain–Fog Conditions Using Monocular Surveillance Imagery
hhttps://www.mdpi.com/2071-1050/18/2/625
JAN
2026
Improve obstacle detection in dense fog using adaptive multi-modal sensor fusion.
Hardware: Gated Camera, 3D LiDAR. Software: AFW-Net, Attention-based Adaptive Fusion, Uncertainty Estimation, Cross-modal Feature Extraction.
Adaptive sensor weighting, Reliable sensor fusion, Robust fog perception
FogGate-YOLO: Traffic Object Detection in Foggy Environments Using Channel Selection Mechanisms
https://www.mdpi.com/1424-8220/26/6/1811
MAR
2026
Develop an ensemble AI framework for accurate vehicle detection and classification under adverse weather.
Design a lightweight object detector specifically optimized for foggy environments.
Achieved 82% AP at 50 m visibility, improving detection by 23.7% over conventional RGB-LiDAR fusion.
Ensemble learning, High detection accuracy, Vision-dependent
Adaptive Sensor Fusion for Robust Perception in Dense Fog: A Gated Vision and LiDAR Integration Framework
hhttps://www.mdpi.com/1424-8220/26/12/3728
JUNE
2026
Outcome
Hardware: RGB Camera.
Software: YOLOv5, YOLOv7, YOLOv8, YOLOv10, DETR-ResNet50, Faster R-CNN, Dynamic Weighting, NMS, Ensemble Learning.
Hardware: RGB Camera.
Software: YOLOv12, A2C2f-FSA Module, Bidirectional Feature Fusion Module (BFFM), GSConv, F-WIoU v3 Loss.
Hardware: RGB Camera, LiDAR. Software: Depth Completion Network with Fog Convolution (DCFC), Flexible Cylindrical Voxel (FCV), Cylindrical Fusion Module (CFM).
Hardware: Monocular CCTV Camera. Software: Koschmieder Scattering Model, Dark Channel Prior, Monte Carlo Simulation, Low Visibility Risk Field Force (LVRFF).
Achieved 96.6% mAP, 94.2% Precision, and 94.1% F1-score for multi-class vehicle detection.
Improved mAP@0.5 by 5.2% (RTTS) and 7.3% (VOC-FOG) while maintaining real-time inference.
mproved detection performance by ≥3.32% over baseline methods on KITTI-C.
Achieved >86% visibility estimation accuracy and effectively identified high-risk driving zones.
LITERATURE SURVEY
Study of the research work

## Slide 4
S.NO
Title of the Paper
Hardware
/Software
Year
Inference
6.
7.
8.
9.
10.
Objective
Multi-Target Tracking with Collaborative Roadside Units Under Foggy Conditions
JAN
2026
Improve foggy 3D object detection using LiDAR-based perception and fog-aware processing.
Fog-aware processing preserves point-cloud features, enabling reliable 3D detection in poor visibility.
3D Vision Object Detection for Autonomous Driving in Fog Using LiDAR
APR
2025
Generate realistic foggy LiDAR data using WGAN–LSTM to improve 3D detector robustness without real fog data collection.
GAN-based fog simulation reduces real-world data dependence and improves autonomous vehicle perception robustness.
Fog-aware features and improved detection heads enhance bounding boxes and reliability for foggy perception.
Simulation of LiDAR Under Fog with Generative Adversarial Networks for Robust 3D Object Detection
OCT
2025
Enhance performance in foggy-weather using a cost-effective vehicle detection system for distance, speed, and TTC-based collision warnings.
Software: SimYOLO-V5s_WIOU detector, Deep-SORT-based tracking
Hardware: RGB cameras with edge-capable platforms for real-time inference
SimSPPF and Wise-IoU improve fog detection reliability, while robust tracking and TTC-based warnings support safer collision avoidance.
Fog-YOLO: A Real-Time Object Detector for Foggy Autonomous Driving Scenarios
FEB
2026
Improve foggy roadside LiDAR tracking by reducing point-cloud noise and enabling collaborative multi-RSU perception.
Develop a low-latency, fog-robust detector for autonomous driving with improved accuracy.
SimYOLO-V5s_WIOU improved fog detection accuracy (up to +17.45% mAP50) on foggy driving, enhanced tracking reliability, and enabled TTC-based graded collision warnings.
Noise-aware denoising and multi-RSU PHD fusion improve foggy LiDAR detection, range, and tracking stability.
ECE-VDTDA: A Robust and Computationally Efficient Collision Avoidance System for Driver Assistance in Foggy Weather
FEB
2026
Outcome
Hardware: Roadside LiDAR-equipped RSUs for fog-affected traffic data collection.
Software: Fog-noise removal using adaptive filtering and multi-RSU cooperative tracking with PHD filtering
Hardware: RGB cameras with GPU-enabled platforms for real-time inference.
Software: Fog-YOLO with fog-aware modules and improved detection head
Hardware: Automotive LiDAR sensors evaluated under foggy conditions.
Software: LiDAR-based 3D detection with fog-mitigation techniques
Hardware: Velodyne VLP-32C LiDAR with fog-chamber and onboard ROS
Software: ROS-based LiDAR processing with WGAN-GP + LSTM fog simulation
Improved detection accuracy by +8% (thin fog) and +29% (thick fog), with enhanced multi-class tracking performance.
Improved mAP over YOLO baseline with better small/occluded object detection in varying fog while maintaining real-time performance.
Improved 3D detection accuracy and recall under fog compared to uncompensated LiDAR baselines.
Generated 80,000 foggy LiDAR frames using WGAN–LSTM, improving 3D detector robustness and reducing the need for real fog data collection.
LITERATURE SURVEY
Study of the research work

## Slide 5
INFERENCE FROM LITERATURE SURVEY

## Slide 6
12-Week Development Sprint
A structured roadmap from literature survey to functional Edge-Al prototype.
Phase & Focus
Week
Phase 1: Foundation
Week 1-2
(Research & Hardware)
Week 3
Week 4
Phase 2: Integration
Week 5
(Interfacing & Data)
Week 6
Week 7
Phase 3: Edge-Al
Week 8
(Algorithm & Alert)
Week 9
Week 10
Phase 4: Finalisation
Week 11
(Prototype & Delivery)
Week 12
Core Activity
Literature Survey, Problem Analysis & Component
Procurement.
STM32/Cortex-M setup and architecture learning.
Sensor Interfacing & ADC Testing.
Data Collection from live moving vehicles.
Initial Signal Processing Implementation.
Vehicle Detection Algorithm (TinyML) Development.
LED, Buzzer, and Display Integration.
System Testing, Calibration, and Optimisation.
Complete Prototype Assembly.
Result Analysis and Performance Evaluation.
Report Writing and PPT Preparation.
Key Milestone
Hardware Procured &
Environment Setup
Successful Sensor Data
Acquisition
Functional Detection
Algorithm
Final Demonstration (Oct 6)

## Slide 7
methodology

## Slide 8
HARDWARE COMPONENTS
TM4C123GH6PM
The TM4C123GH6PM is the central microcontroller of our project that acquires microphone signals, processes vehicle detection logic, and controls the OLED display, buzzer, and LEDs to provide real-time collision warnings in foggy conditions.

## Slide 9
HARDWARE COMPONENTS
TM4C123GH6PM

## Slide 10
HARDWARE COMPONENTS
MAX4466 Analog Microphone Module
SSD1306 OLED Display
ST Link V2 Programmer
BUZZER
LEDS AND RESISTORS
BREADBOARD
JUMPER WIRES
USB CABLE

## Slide 11
DEVELOP SIMULATION MODEL
The Simulink model represents the proposed ghost vehicle detection system, where vehicle-generated pressure waves are simulated and processed through the MAX4466 sensor model. The STM32 Cortex-M4 processing unit performs signal analysis and generates real-time alerts through LED, buzzer, and OLED display when a vehicle is detected

## Slide 12
BLOCK DIAGRAM

## Slide 13
HARDWARE
MODEL

## Slide 14
RESULTS
  Successfully interfaced the MAX4466 microphone sensor with the TM4C123GH6PM microcontroller.
  Real-time ADC values were successfully acquired from the pressure-wave sensor.
  The ADC reading was displayed correctly on the OLED display via I²C communication.
  The display confirmed that the Ghost Vehicle Detection System was initialized and functioning properly.
  The prototype successfully demonstrated real-time acoustic pressure-wave monitoring.
  The obtained results validate the feasibility of the proposed sensing approach for future ghost vehicle detection.

## Slide 15
[1]. Zhang, Fengyuan, et al. "Adaptive sensor fusion for robust perception in dense fog: A gated vision and LiDAR integration framework." Sensors 26.12 (2026): 3728.
[2]. Q. Yuan et al., "Ensemble Artificial Intelligence Framework for Real-Time Automatic Vehicle Detection and Classifications," in IEEE Access, vol. 14, pp. 16034-16050, 2026, doi: 10.1109/ACCESS.2026.3657829.
keywords: {Vehicle detection;Artificial intelligence;Accuracy;Real-time systems;Detectors;YOLO;Autonomous vehicles;Automobiles;Robustness;Feature extraction;Deep learning;dynamic weighting;ensemble learning;real-time vehicle detection},
[3].Wang, Quanxiang, Zhaofa Zhou, and Zhili Zhang. "Fog-YOLO: A Real-Time Object Detector for Foggy Autonomous Driving Scenarios." Symmetry 18.2 (2026): 322.
[4]. Zhang, Bingli, et al. "FogFusion: Robust 3D object detection based on camera-LiDAR fusion for autonomous driving in foggy weather conditions." Proceedings of the Institution of Mechanical Engineers, Part D: Journal of Automobile Engineering 240.4 (2026): 2312-2322.
[5].Xie, Zilong, et al. "Dynamic Visibility Recognition and Driving Risk Assessment Under Rain–Fog Conditions Using Monocular Surveillance Imagery." Sustainability 18.2 (2026): 625.
REFERENCES

## Slide 16
Thank You !